## Slide 1: Networking for Software Developers
Lecture 4 – Part I – Summer 2024

## Slide 2: Agenda
Networking Basics
Network Devices
Packets & Wireshark

## Slide 3: Networking Basics

## Slide 4: Networks
Comprises of two or more systems that are connected with the purpose of transmitting, exchanging or sharing data and resources
Classified by many criteria:
  Medium for signals
  Bandwidth
  Protocols for network traffic
  Network size
  Topology
  Traffic control mechanism
  Organizational intent
  Etc.

## Slide 5: Features of Networks
Generality
  Built with general-purpose resources and services to support wide range of applications
Multi-perspective
  Services to support applications’ functional and non-functional requirements
  Administer and manage systems and related networks
  Optimize cost, performance, scalability, security, etc.

## Slide 6: Features of Networks
Connectivity
  Majority of computer networks are packet-switched, where nodes send discrete blocks of data to each other
  Network can have node directly or indirectly connected to each other
Cost-Effective Resource Sharing
  Support communication between all nodes with the ability to exchange messages via multiplexing and demultiplexing

## Slide 7: Features of Networks
Support for Common Services
  Allow application processes to communicate via a logical channel using common communication requirements
Reliability
  Require recovery from physical and software-based issues and failures
Manageability
  Support manual/automated activities to ensure networks are running correctly and correctly configured

## Slide 8: Network Architecture
Network topology – layout, pattern, or organizational hierarchy of the interconnection of network hosts
  The topology can affect throughput and reliability
  General principle: greater number of interconnections yields a more robust network is; however, it increases expenses to install and maintain

## Slide 9: Network Architecture
Common topology patterns include:
  Bus network – all nodes are connected to a common medium
  Star network – all nodes are connected to a central node (e.g., wireless LAN)
  Ring network – each node is connected in a closed-loop configuration
  Mesh network – nodes are connected dynamically and non-hierarchically to as many other nodes as possible
  Tree network – nodes are arranged hierarchically (e.g., hub and spoke model )

## Slide 10: Network Architecture
Application
Presentation
Session
Transport
Networking
Datalink
Physical
Human-computer interaction layer and facilitates access to networks services
Ensures that data is in a usable format and provides encryption services
Maintains connections and controls ports and sessions
Transmits data using transmissions protocols
Decides physical path of the data
Defines the format of the data on the network
Transmits raw bits streams over physical medium

## Slide 11: Network Architecture
Application
Presentation
Session
Transport
Network
Data Link
Physical
OSI Model
Network Access
Internet
Transport
Application
TCP/IP Model
HTTP
DNS
FTP
FTP
SMTP
SSH
TCP
UDP
IP (ARP, IGMP, ICMP)
Ethernet
IEEE 802.11
Frame Relay
PCIe
Protocols

## Slide 12: Practical Approach?

## Slide 13: Deployment Diagram
Structural UML diagram used in modeling the physical aspects of an object-oriented system
  Depicts and describes the physical deployment of information generated by the software on hardware components
  Illustrate the runtime processing for hardware, communications approaches and protocols between components, deployment controls, etc.

## Slide 14: Deployment Diagram
Node
Relationships
Artifact
Component

## Slide 15: Example

## Slide 16: Network Devices

## Slide 17: Network Devices
A variety of devices support networks:
  Modem
  Router
  Switch
  Access Point
  Firewall
  Repeater
  Network Interface Card
  Hub

## Slide 18: Network Devices
Phone
Tablet
Laptop
Access Point
Desktop
Desktop
Desktop
Switch
Modem
Workstation
Server
Firewall
Internet

## Slide 19: Network Devices
Modems (modulators-demodulators) – network hardware that converts digital signals into analog signals (and vice-versa)
  Connected to a line from the ISP (e.g., Rogers, Bell, etc.)
Incoming signal is analog (i.e., useless for any software application)
  Recreates the frames and passed to different layers for processing
  Resulting frames or packets are sent via Wi-Fi or wire that will be consumed by the device NIC
Outgoing signal is digital, which is are converted by the modem into analog signal (of different frequencies)
Operates on the Physical and Data Link layers

## Slide 20: Network Devices
Router – network hardware that serves as a multiport device and improves network efficiency
  Stores information about the network and devices within the network
  Determines best route for information, priority of networked devices, etc.
  Provide safeguards (e.g., filtering firewalls and use ACLs)
  Divide and connect internal networks into two or more subnetworks, or interconnect two or more heterogeneous networks
Operates on the Network layer

## Slide 21: Network Devices
Switch – network hardware that intelligently routes data packets based on their IP addresses and ports
  Stores and maintains limited routing information for the internal network
  Facilitates connections to network hardware and systems (e.g., routers, hubs, etc.) by reading hardware addresses of incoming packets and transmitting the packets to the appropriate destination
Different variants of switches: unmanaged, managed, modular, PoE, etc.
Operates on the Data Link and Network layers

## Slide 22: Network Devices
Access Point (AP) – network hardware that connects a wired network to wireless devices or a router passing data transmissions between APs
  Wireless access points (WAPs) consist of a transmitter and receiver (transceiver) device used to create a WLAN to connect between WLANs and a wired Ethernet LAN
  Different variants of APs: Bridge AP, Repeater AP, etc.
Provides many ports to increase the network’s size, firewall capabilities, encryption (e.g., WEP, WPA, WPA2), etc.
Note: AP is not a hotspot which is a physical location to access Wi-Fi
Operate on the Data Link layer

## Slide 23: Network Devices
Firewall – monitors and controls incoming and outgoing network traffic based on predetermined security and access rules
  Inserted in connections between trusted internal networks and potentially insecure external networks (e.g., Internet)
  Establishes a barrier between the internal and external networks
Configured to reject access requests from unrecognized sources while allowing actions from recognized ones
Associated with on a discrete device, host machine, proxy-server, etc.
Provide functionality: NAT, intrusion prevention, application awareness, etc.

## Slide 24: Network Devices
Repeater – network hardware that receives a signal and retransmits it at a higher level or higher power so that the signal can cover longer distances
  Also, regenerates the signal over the same network before the signal becomes too weak or corrupted over the extended length
  Different variants of Repeaters: Analog and Digital Repeater
Operate on the Physical layer

## Slide 25: Network Devices
Network Interface Card (NIC) – network hardware that serves as an adapter to connect a host to the network via a physical or wireless connection
  Implemented as a daughter card or directly integrated onto the motherboard
  Most computers have at least two NICs – wired and wireless
  Ethernet network controllers typically supports 10, 100 or 1000 MB/s
Operate on the Physical and Data Link layers

## Slide 26: Network Devices
Other devices include:
  Gateways
  Hubs
  Bridges
  Etc.

## Slide 27: Note on Operating Systems
In the past if an operating system does not directly support networking, then device driver (software that extends the OS) provides the necessary support
Unix and Linux were designed and built with networking in mind
Most modern OS supports networking this support includes the following:
  Implementation of TCP/IP
  Support for hardware (e.g., NICs, Bluetooth)
  Utilities such as ping
  Multi-user support
  Device sharing
  Authentication and authorization

## Slide 28: Class Exercise